## Slide 1: String Instructions

## Slide 2
A string of characters are stored in memory as consecutive memory locations.
Each character is represented by its ASCII equivalent.
For a string, we need 1. Starting/ end address and 2. Length of the string
The length of the string is usually stored as count in the CX register.
8086 supports a set of string manipulation instructions
For string traversal Direction Flag is used to increment or decrement the pointer.

## Slide 3
REP : Repeat Instruction Preview
MOVSB/ MOVSW : Move string byte or string word
CMPS : Compare string byte or string word
SCAS : Scan string byte or string word
LODS : Load string byte or string word
STOS : Store string byte or string word

## Slide 4
REP
Used as a prefix to other instructions
Instruction is executed repeatedly until the CX register becomes zero
At each iteration CX is automatically decremented by one
When CX = 0, execute the next instruction
REPE/ REPZ - repeat operation while equal/ zero (For CMPS and SCAS only)
REPNE / REPNZ = repeat operation while not equal or not zero (For CMPS and SCAS only)

## Slide 5: MOVSB / MOVSW
Move string byte or string word from one location (DS:SI source) to another location (ES:DI destination)
Source string starting address in DS + SI ( 10H * DS + SI )
Destination string starting address in ES + DI ( 10H * ES + DI )
REP instruction prefix is used with MOVS to repeat it by the value in CX register
CX = length of the byte string / word string
No flags are affected by this instruction
After MOVS is executed once, index registers are automatically updated and CX is decremented
Increment / Decrement of SI / DI are done based on DF
If DF = 0, then Index Registers are incremented, else they are decremented

## Slide 6: CMPS: Compare String Byte or String Word
Compare 2 strings of bytes or words
CX = length of the string
If strings are equal, zero flag is set
DS:SI and ES:DI point to 2 strings
REP is used to repeat the instruction until CX = 0 or the condition specified by the REP instruction is false
Byte by byte or word by word comparison continues till a mismatch is found
Once mismatch is found, CF and ZF are modified

## Slide 7: SCAS : Scan string byte or string word
Scans a string of bytes or words for an operand byte or word specified in register AL or AX
String is pointed by ES:DI pair
CX = length of the string
DF = controls the mode for scanning of the string
On match, execution stops and ZF is set
REPNE is used with SCAS
Pointers and Counters are updated till a match is found

## Slide 8: LODS: Load string byte or word
Loads AL/ AX register by the content of the string pointed to by DS:SI
SI is modified automatically depending on DF
For byte transfer, SI is modified by 1
For word transfer, SI is modified by 2
No other flags are affected by this instruction

## Slide 9: STOS: Store string byte or word
Stores AL/AX register contents to a location pointed by ES:DI
DI is modified accordingly
No flags are affected
DF controls the string instruction execution
SI and DI are modified after each iteration automatically
DF = 1, then SI/DI in autodecrement mode
In autodecrementing mode, the strings are referred by their ending address
DF = 0, then SI/DI in autoincrementing mode
In autoincrementing mode, the strings are referred by their starting address